# Schematic files format:

## Units
Sizes and coordinates are given in mils (1/1000 inch)
## Header
Format :
EESchema Schematic File Version 1
LIBS: libraries list (not used, for information only).
EELAYER nn mm (nn mm not used, reserved)
EELAYER END
$Descr Sheet size dimx dimy (sheet size = A4..A0 ou A..E)
Title block description (Texts of the title block)
$EndDescr

EESchema Schematic Spins Version 1
LIBS:brooktre, cypress, ttl, power, linear, memory, xilinx, idiot, aaci, INTEL, special, device, dsp
EELAYER 20 0
EELAYER END
$Descr A3 16535 11700
Sheet 1 4
""
Date “28 DEC 1996”
Rev ""
Comp ""
Comment1 ""
Comment2 ""
Comment3 ""
Comment4 ""
$EndDescr

## Description of a component
Format:
$Comp
L name reference
U N mm time_stamp
P posx posy
List of fields:
F field_number “text” orientation posX posY size Flags (see below) hjustify vjustify/italic/bold “name”
1 posx posy (redundant: not used)
A B C B ( orientation matrix with A, B, C, D = - 1, 0 or 1)
$EndComp
Description of the fields:
F n “text” orientation posx posy dimension flags hjustify vjustify/italic/bold “name”
with n = field number (reference field = 0, value field = 1, N = 0..11 or more)
orientation = H (horizontal) or V (vertical).
- n = field number :
- reference = 0.
- value = 1.
- Pcb FootPrint = 2.
- User doc link = 3.	At present time: not used (reserved)
- n = 4..11 = fields 1 to 8 (since January 2009 more than 8 field allowed, so n can be > 11.
- text (delimited by double quotes)
- orientation = H (horizontal) or V (vertical).
- position X and Y
- dimension (default = 50)
- Flags: visibility = 0 (visible) or 1 (invisible)
- hjustify vjustify = L R C B or T
- L= left
- R = Right
- C = centre
- B = bottom
- T = Top
- Style: Italic = I or N ( since January 2009)
- Style Bold = B or N ( since January 2009)
- Name of the field (delimited by double quotes) (only if it is not the default name)
Note: vjustify, Italic and Bold are in the same 3 chars word.
Example:

Comp
L CONN_3 JP3
U 1 1 329879E1
P 1200 2000
F 0 “JP3” H 1250 2200 60 0000 C CNN
F 1 “CONN_3” V 1350 2000 50 0000 C CNN
F 4 "example" H 8000 4350 60 0000 C CIB "myfield"
    1 1200 2000
   1 0 0 - 1
$EndComp

## Description of a NoConnect symbol
Format: NoConn ~ posx posy
Example:
NoConn ~ 13400 5500

## Description of a hierarchical sheet symbol
Format:
$Sheet
S posx posy dimx dimy
List of Sheet Labels
$EndSheet
Format of Sheet Labels
Fn “text” forms side posx posy dimension
With:
n = sequence number (0..x).
n = 0: name of the corresponding schematic file.
n = 1: name of the sheet of hierarchy.
form = I (input) O (output) B (BiDi) T (tri state) U (unspecified)
side = R (right) , L (left)., T (tpo) , B (bottom)
Example:

$Sheet
S 1800 1600 1500 1500
F0 “PROGALIM.SCH” 60
F1 “PROGALIM.SCH” 60
F2 “CLK” O R 3300 1800 60
F3 “/RESET” O R 3300 2000 60
F4 “VPWR” O R 3300 2700 60
F5 “/HALT” O R 3300 2100 60
F6 “TRANSF1” I L 1800 1900 60
F7 “TRANSF2” I L 1800 2000 60
F8 “3.84MH” O R 3300 2200 60
$EndSheet

## Description of a text note
Format: Text Notes posx posy orientation dimension ~
Text
Example:
Text Notes 2100 3250 1 60 ~
TOTO

## Description of a Global Label
Format: Text GLabel posx posy orientation dimension shape
Text
Example:

Text GLabel 3100 2500 2 60 UnSpc
TITI
Text GLabel 3150 2700 1 60 3State
3STATES
Text GLabel 2750 2800 0 60 UnSpc
BIDI
Text GLabel 2750 2650 0 60 Output
GLABELOUT
Text GLabel 2750 2400 0 60 Input
RESET

## Description of a Hierarchical label
Format: Text HLabel posx posy orientation dimension shape
Text
Example:

Text HLabel 3400 2000 0 60 Input
/RESET

## Description of a label
Format: Text Label posx posy orientation dimension ~
Text
Example:

Text Label 3400 2000 0 60 ~
/RESET

## Description of a junction
Format: Connection ~ posx posy
Example:

Connection ~ 13300 6500

## Description of a wire segment (Wire)
Format:
Wire Wire Line
startx starty endx endy
Example:

Wire Wire Line
3300 1800 3900 1800

## Description of a Bus segment
Format:
Wire Bus Line
startx starty endx endy
Example:

Wire Bus Line
3900 5300 4500 5300

## Description of a dotted line segment
Format:
Wire Notes Line
startx starty endx endy
Example:

Wire Notes Line
2850 3350 2850 3050

## Description of a bus entry
Format:
For an entry wire/bus :
Wire Wire Bus
startx starty endx endy
For an entry bus/bus :
Wire Bus Bus
startx starty endx endy
Example:

Entry Wire Bus
4100 2300 4200 2400
Entry Bus Bus
4400 2600 4500 2700

## Description of a Bitmap Image
Bitmaps are considered to be 300x300 pixels per inch.
A scaling factor is applied by Eeschema to adjust the actual bitmap size on screen.
Format:
$Bitmap
Pos posx posy
Scale scale value (float). This is the user scalin factor used to display the bitmap.
Data
Bitmap data , PNG format, in hexadecimal.
Each byte is coded by 2 hexadecimal digits.
Bytes are separated by a space.
EndData
$EndBitmap

Example:

$Bitmap
Pos 7450 5600
Scale 1,000000
Data
89 50 4E 47 0D 0A 1A 0A 00 00 00 0D 49 48 44 52 00 00 01 00 00 00 01 00 08 06 00 00 00 5C 72 A8
66 00 00 00 04 73 42 49 54 08 08 08 08 7C 08 64 88 00 00 00 09 70 48 59 73 00 00 1B 58 00 00 1B
….
EndData
$EndBitmap