eeschema

# Hierarchical schematics.
## Presentation.
A hierarchical representation is generally a good solution for projects bigger than a few sheets. If you want to manage this kind of project, it will be necessary to :
- Use large sheets, which results in printing and handling problems.
- Use several sheets, which leads you to a hierarchy structure.
The complete schematic then consists in a main schematic sheet, called root sheet, and sub-sheets constituting the hierarchy.
Moreover, a skillful subdividing of the design into separate sheets often improves on its legibility.
From the root sheet, you must be able to find all sub-sheets.
Hierarchical schematics management is very easy with Eeschema, thanks to an integrated “hierarchy navigator” (button of the upper and right toolbar, further detailed).
In fact, there are two types of hierarchy (that can exist simultaneously):
The first one has just been evoked and is of general use.
The second consists in creating components in the library that appear like traditional components in the schematic, but which actually correspond to a schematic which describes their internal structure.
This second type is rather used to develop integrated circuits, because in this case you have to use function libraries in the schematic you are drawing.
Eeschema currently doesn't treat this second case.
A hierarchy can be:
- simple: a given sheet is used only once
- complex: a given sheet is used more than once (multiples instances)
- Flat which is a simple hierarchy, but connections between sheets are not drawn.
Eeschema knows all these hierarchies.
The creation of a hierarchical schematic is easy, the whole hierarchy is handled starting from the root schematic, as if it were only one schematic.
The two points to be known are :
- How to create a sub-sheet.
- How to build electric connections between sub-sheets.
## Navigation in the Hierarchy
It is very easy thanks to the navigator (tool of the horizontal toolbar) shown here :

Each sheet is reachable, clicking its name.
Fast navigation:
Right click on a sheet name, and choose enter sheet.
You can also quickly reach the root sheet, or a sub-sheet thanks to the tool of the right vertical toolbar.
After tool selection :
- Click on a sheet name to selection this sheet.
- Click elsewhere to select the main sheet.
## Local, hierarchical and global labels .
### properties:
Local labels (tool ) are connecting signals only within a sheet
hierarchical labels (tool ) are connecting signals only within a sheet and to a hiérarchical pin placed in the parent sheet.
Global labels (tool ) are connecting signals across all the hierarchy.
Power pins (type power in and power out) invisibles are like global labels because they are seen as connected between them across all the hierarchy.
### Notes:
Within a hierarchy (simple or complex) one can use both hierarchical labels and global labels.
## Hierarchy Creation. Headlines.
You have to :
- Place in the root sheet a hierarchy symbol called “sheet symbol”.
- Enter into the new schematic (sub-sheet) with the navigator and draw it, like any other schematic.
Draw the electric connections between the two schematics by placing Global Labels (HLabels) in the new schematic (sub-sheet), and labels having the same name in the root sheet, known as SheetLabels. These SheetLabels will be connected to the sheet symbol of the root sheet to the other elements of the schematic like standard component pins.
## Sheet symbol.
Draw a rectangle defined by two diagonal points symbolizing the sub-sheet.
The size of this rectangle must allow you to place later particular labels, hierarchy pins, corresponding to the global labels (HLabels) in the sub-sheet .
These labels are similar to usual component pins.
Select the tool .
Click to place the upper left corner of the rectangle. Click again to place the lower right corner, having a large enough rectangle.
Example :

You will then be prompted to type a filename and a sheet name for this sub-sheet (in order to reach the corresponding schematic, using the hierarchy navigator).

You must give at least a file name. If there is no sheet name, the filename will be used as sheet name (usual way to do that).
## Connections: Hierarchy pins.
You will create here points of connection (Hierarchy pins) for the symbol which has been just created.
These points of connection are similar to normal component pins, with however the possibility to connect a complete bus with only one point of connection.
There are two ways to do this:
- Place the different pins before drawing the sub-sheet (manual placement).
- Place the different pins after drawing the sub-sheet, and the global labels (semi-automatic placement).
The second solution is quite preferable, as much as possible.
Manual placement:
- To select the tool .
- Click on the hierarchy symbol where you want to place this pin.
See below an example of the creation of the hierarchical pin called “CONNEXION”.

You can then define its graphical attributes, size ( Right click and select Edit in the PopUp menu) :

Various pin symbols are available :
- Input
- Output
- BiDir
- TriState
- NotSpecified
These pin symbols are only graphic enhancements, and have no other role.
Automatic placement:
- Select the tool .
- Click on the hierarchy symbol from where you want to import the pins corresponding to global labels placed in the corresponding schematic. A hierarchical pin appears, if a new global label exists, i.e. not corresponding to an already placed pin.
- Click where you want to place this pin.
All necessary pins can thus be placed quickly and without error. Their aspect is in accordance with corresponding global labels.
## Connections: Hierarchical labels.
Each pin of the sheet symbol just created, must correspond to a label called hierarchycal Label or HLabel in the sub-sheet.
HLabels are similar to labels, but they provide connections between sub-sheet and root sheet.
The graphical representation of the two complementary labels (pin and HLabel) is similar.
HLabel creation is made with the tool .
See below a root sheet example :

Notice pins TRANSF1 and TRANSF2, connected to connector JP3.
Here are the corresponding connections in the sub-sheet :

You find again, the two corresponding HLabels, providing connection between the two hierarchical sheets.
Note:
You can use HLabels and Hierarchy pins to connect two buses, according to the syntax (Bus [N. .m]) previously described.
### Labels, HLabels and Invisible Power Pins.
Here are some comments on various ways to provide connections, others than wire connections.
#### Simple labels.
The simple labels have a local capacity of connection, i.e. limited to the schematic sheet where it is placed.
This is due to the fact that :
- Each sheet has a sheet number.
- This sheet number is associated to the Label.
Thus, if you place the label “TOTO” in sheet n° 3, in fact the true label is “TOTO_3“.
If you also place a label “TOTO” in sheet n° 1 ( root sheet) you place in fact a label called “TOTO_1“, different from “TOTO_3“.
This is always true, even if there is only one sheet.
#### Hierarchical labels.
What is said for the simple labels is also true for hierarchical labels or HLabels.
Thus in the same sheet, a HLabel “TOTO” is considered to be connected to a local label “TOTO”, but not connected to a HLabel or label called “TOTO” in another sheet.
However a HLabel is regarded as to be connected to the corresponding SheetLabel symbol in the hierarchical symbol placed in the root sheet.
#### Invisible Power pins.
It was seen that they were connected together if they had the same name.
Thus all the power pins declared “Invisible Power Pins“ and named VCC are connected and form the equipotential VCC, whatever the sheet they are placed on.
This explains that if you place a VCC label in a sub-sheet, it will not be connected to VCC pins, because this label is actually VCC_n, where n is the sheet number.
If you want this label VCC to be really connected to the equipotential VCC, it will have to be explicitly connected to an invisible power pin, thanks to a VCC power port.

## Complex Hiérarchy
Here is an example : The same schematic is used twice (two instances).
The two sheets share the same schematic because the filename is the same for the two sheets ("other_sheet.sch").
But the sheet name must be different.

## Flat Hierarchy
One can create a project using many sheets, without creating connections between these sheets (flat hierarchy) if the next rules are used:
- One must creates a root sheet containing the other sheets, which acts as a link between the others sheets.
- No explicit connections are needed.
- All connections between sheets will use Global Labels instead of hierarchical labels.

Here is the root sheet:

Here is the two pages, connected by global labels:

Look at global labels