# Main menu
## File menu

Load Schematic Project	Load a diagram and its hierarchy
Save Schematic project	Save current sheet and all its hierarchy.
Save Current sheet	Save current sheet.
Save Current sheet as...	Save current sheet with a new name.
Print	Access to print menu (See also chap “Print and Plot”).
Plot	Plot in Postscript HPGL or SVF format (See chap “Print and Plot”).
Exit	Quit without saving.

## Preferences menu

Libs and Dir	Select libraries and the library's path
Colours	Select colours.
Options	Display options (Units, Grid size.).
Read preferences / Save preferences	Read and Save configuration file.
Show Current Hokey List	Shows the current hotkeys, Same as ?
Create Hotkey config file	Create a hotkeys config file, which can be modified (by a text editor), for those who want change the default hotkeys
Reread Hotkey config file	Read the current hotkeys file, after editing.
Edit Hotkey config file	Launches a text editor and edit the hotkeys config file previously created
Hotkey config file	Set the directory used to read/store the hotkeys config file / (Home directory or kicad/template)

### Preferences menu / Libs and Dir

Eeschema configuration is essentially :
- Library's path.
- Library's list.

The configuration parameters are saved in the .pro file.
Different configuration files in different directories are possible.
Eeschema seeks and uses by decreasing priorities :
1. The configuration file (project>.pro) in the current directory.
2. The kicad.pro configuration file in the kicad directory. This file can thus be the default configuration.
3. Default values if no file is found. It will at least then be necessary to fill out the list of libraries to load, and then save the configuration.
### Preferences menu / Colours

Various drawing elements, colour selection and background colour (black or white only).
### Preferences / Options

Show Grid :
If checked : display grid.
Grid Size:
To work with normal grid (0,050 inches or 1,27 mm). Smaller grids are used for component building.
Show Pins:
Display invisible pins if checked (allows the display of power pins).
Units:
Select the display and the cursor coordinate units (Inches or Millimetres).
Wire / Bus orientation
Horiz/vertical checked : only horizontal or vertical wires or buses are allowed.
Active Any : all orientations are allowed.
Auto Pan :
If checked, automatically shifts the window if the cursor leaves the window, during wire drawing, or element moving.

Element repeat:
X Step :
shift value on X axis during element duplication (usual value 0)
Y Step :
shift value on Y axis during element duplication (usual value is 0,100 inches or 2,54 mm)
Label Step :
Increment during duplication of texts ending in a number, such as bus members (usual value 1 or - 1).
### Preferences / Language
Use default mode.
Other languages are available.
Eeschema has to be restarted.
Useful mainly for maintenance purpose.
## Help menu
Access to on-line help (this document) and also for checking the current version of Eeschema (Eeschema about).