# Creating the copper zones
Copper zones must be created when all the routing is finished.
After a route modification, zones must be deleted and recreated.
Pads of the net must be already connected by standard tracks. Do not expect connecting pads through the zone.
This is because:
- All board characteristics (pads, board edges) must be known.
- D.R.C. does not test zones (because of time computation problems).

Copper zones (Usually ground and power planes) are usually attached to a net.
In order to create a copper zone one must:
- Select the net (Highlight this net), to attach the zone to this net.
- Create the zone limit (If no, All the board will be filled.)
- Fill the zone from a starting point.
A zone is always created all of a piece, to insure there is not any unconnected copper block.
## Net selection:
Use the tool , and click on a pad connected to the net, which must be highligted.
## Creating a zone:
### Creating the zone limits:
Use the tool .
Choose the layer for the zone.
Draw the zone limit, on this layer.
This zone limit is a polygon, created by a click (left button) for each corner.
A double click ends the polygon.
The polygon will be automatically closed. If the starting point and the ending point are not at the same coordinate, Pcbnew will add a segment from the end point to the start point.
Here is a zone limit created (polygon in thin line):

### Filling the zone:
Tje filling zone is initiated from a starting point (Mouse cursor).
In order to do it, when the edge zone is finished, put the mouse cursor on a starting point for the filling. This point can be inside or outside the polygon, and on a free spot.
Click the right mouse button. This menu will be showed:

Activate the "Fill" button
Here is the filling result for a starting point inside the polygon:

Here is the filling result for a starting point outside the polygon:

The polygon is a frontier for filling.
Note:
you can use many polygons to create a complex limit. Here is an example:

Here is the filling result for a starting point inside the large polygon and outside the small polygon:

## Fill Options:

One must choose:
- The working grid for filling.
- The clearance.
- How the pads are drawn inside the zone (or connected to this zone).
### Working grid for filling.
The smaller the filling grid is, the better the filling is.
However, the filling is made with horizontal and vertical track segments, if the grid is small, board files can be very larges (several Mo.).
A 0.01 inch grid is a good compromise.
### Clearance
A good choice is a grid a bit bigger than the routing grid.
### Pad options
Pads of the net can either be included or excluded from the zone, or connected by thermal reliefs.
- If included, soldering and unsoldering can be very difficult.
- If excluded, the connection to the zone is not very good.
- A thermal relief is a good compromise.

Here is the result for the 3 options:

Include Pads
Exclude Pads
Thermal relief. / Pad is connected by 4 track segments. / The segment width is the current value used for the track width.