# Main menu
## File menu

New	Clear current schematic and initialize a new one
Open	Load a schematic hierarchy
Open Recent	Open a list of recent opened files for loading
Save Whole Schematic project	Save current sheet and all its hierarchy.
Save Current Sheet Only	Save current sheet, but not others in a hierachy.
Save Current sheet as...	Save current sheet with a new name.
Print	Access to print menu (See also chap “Print and Plot”).
Plot	Plot in Postscript HPGL or SVF format (See chap “Print and Plot”).
Quit	Quit without saving.

## Preferences menu
### Preferences!

Library	Select libraries and the library's path
Colors	Select colours.
Options	Display options (Units, Grid size.).
Language	Access to the current list of translations. / Use default. / Mainly for translators and developers
Read preferences / Save preferences	Read and Save configuration file.
Hotkeys	Access to the hot keys menu

### Hotkeys sub menu:
List Current Keys	Shows the current hotkeys, Same as ?
Edit Hokeys	Launch the hotkeys editor
Export Hotkeys Config	Create a hotkeys config file.
Import Hotkeys Config	Read a previously exported hotkeys config file.

### Preferences menu / Libs and Dir

Eeschema configuration is essentially :
- Library's path.
- Library's list.

The configuration parameters are saved in the .pro file.
Different configuration files in different directories are possible.
Eeschema seeks and uses by decreasing priorities :
1. The configuration file (project>.pro) in the current directory.
2. The kicad.pro configuration file in the kicad directory. This file can thus be the default configuration.
3. Default values if no file is found. It will at least then be necessary to fill out the list of libraries to load, and then save the configuration.
### Preferences menu / Colours

Various drawing elements, colour selection and background colour (black or white only).
### Preferences / Options

Measurement units:	Select the display and the cursor coordinate units (Inches or Millimetres).
Grid Size:	Grid size selection. / One must work with normal grid (0,050 inches or 1,27 mm). Smaller grids are used for component building.
Default line width:	Pen size used to draw objects that do not have a specified pen size.
Default text size:	Value used when creating new texts or labels
Repeat draw item horizontal displacement	shift value on X axis during element duplication (usual value 0) / (after placing an item like a component, label or wire, a duplication is made by the Inser key)
Repeat draw item horizontal displacement	shift value on Y axis during element duplication (usual value is 0,100 inches or 2,54 mm)
Repeat label increment:	Increment during duplication of texts ending in a number, such as bus members (usual value 1 or - 1).
Show Grid :	If checked : display grid.
Show hidden pins:	Display invisible (or hidden) pins . / If checked, allows the display of power pins.
Enable automatic panning	If checked, automatically shifts the window if the cursor leaves the window, during wire drawing, or element moving.
Allow buses and wires to be placed in H or V orientation only	If checked buses and wires can be only vertical or horizontal. / Else buses and wires can be placed in any direction.
Show page limit	If checked, shows the page limits on screen.

### Preferences / Language
Use default mode.
Other languages are available mainly for maintenance purpose.
## Help menu
Access to on-line help (this document) and also for checking the current version of Eeschema (Eeschema about).