# Routing PCBs

## Current settings:
Current settings are displayed on the toolbar:

This toolbar allows you to select values already used (if any).
## General Options.

For tracks creation, parameters are:
Tracks 45 Only: Directions allowed for track segments are 0, 45 or 90 degrees
- Double Segm Track: When creating tracks, 2 segments will be displayed.
- Tracks Auto Del: When recreating tracks, the old one will be automatically delete if it is redundant.
- Magnetic Pads: The graphic cursor goes to pad, center when entering the pad area.
- Magnetic Tracks: The graphic cursor goes to track axis.
## Choosing routing parameters
The choice is made in the menu: Dimensions ->Tracks and Vias.
The dimensions are given in inches or mm, depending upon the active units.
Reminder: 2.54 cm = 1 inch (or " ) = 1000 mils = 10000 tenths of mils.

When entering a new value for via size and track width, old values are stored and are easily selectable by the toolbar (or the popup menu)
### Global Parameter.
They are:
- Clearance (minimum distance between tracks, vias and pads).
- Mask clearance: margin between pads and mask, for mask layers.
### Track Parameters.
Choose the current track width and the current via size.
### Via Parameters.
Pcbnew handles 3 types of vias:
- The through via (usual vias).
- Blind or buried vias,.
- Micro Vias, like buried vias but restricted to an external layer to its nearest neighbor.
  They are intended to connect BGA to the nearest inner layer. the diameter is usually very small and they are drilled by laser.
By default, all vias have the same drill value.
But one can set a specific drill value to some vias (Alternate Via Drill).
The Popup menu allows to set this specific drill value to one (or many) vias.

If many vias must have a specific drill value, the easiest way is:
- Use a specific diameter for these vias.
- Set an alternate drill value.
- Use Set via hole to alt value for one of these vias.
- Use Export via hole to others id. vias.
## Typical dimensions for different PCB classes
### Track width
Use the largest possible value and conform to the minimum sizes given here:
Units	CLASS 1	CLASS 2	CLASS 3	CLASS 4	CLASS 5
mm	0,8	0,5	0,4	0,25	0,15
1/10mils	310	200	160	100	60

### Insulation (clearance)
Unité	CLASS 1	CLASS 2	CLASSE3	CLASS 4	CLASS 5
mm	0,70	0,5	0,35	0,23	0,20
1/10mils	270	200	140	90	80

Usually, the minimum clearance is very similar to the minimum track width.
## Some typical combinations
### 'Rustic'
- Clearance: 0.35mm (0.0138 inches).
- Track width: 0.8mm (0.0315 inches).
- Pad diameter for ICs and vias: 1.91mm (0.0750 inches ).
- Pad diameter for discrete components: 2.54mm (0.1 inches).
- Ground track width: 2.54mm (0.1 inches).

### 'Standard'
- Clearance: 0.35mm (0.0138 inches).
- Track width: 0.5mm (0.0127 inches).
- Pad diameter for ICs: make them elongated in order to allow tracks to pass between IC pads and yet have the pads offer a sufficient adhesive surface (1.27 x 2.54 mm -->0.05x 0.1 inches).
- Vias : 1.27mm (0.0500 inches).

## Manual routing
Manual routing is recommended, because it is the only method offering control of routing priorities. For example, is is preferable to start by routing power tracks, making them wide and short and keeping analog and digital supplies well separated. Then sensitive signal tracks should be routed. Amongst other problems, automatic routing often requires many vias. However, automatic routing can offer useful insight into the positioning of modules. With experience, you will probably find that the automatic router is useful for quickly routing the 'obvious' tracks, but the remaining tracks will best be routed by hand.

### Help when creating tracks:
Pcbnew can display the full ratsnest, if the toll is activated.
The tool allows to highlight a net (click to a pad or an existing track to highlight the corresponding net net).
The DRC checks in real time tracks when creating them. One cannot create a track which does not match the DRC rules.
It is possible to disable DRC by activate , but it is very dangerous. Use it only in specific caes.
### Creating tracks:
Access by
A new track must starts on a pad or on an other track, because Pcbnew must knows the net used for the new track (in order to match the DRC rules).

When creating a new track, Pcbnew shows links to nearest not connected pads (link number set in option "Max. Links" in General Options.
Finish the track by a double click, or by the Popup menu or by the hot key:

### Moving and dragging tracks
When the tool is active, the track where the cursor is pointed to can be moved with the hotkey 'm'. If you want to drag the track you use the hotkey 'g'.
### Via Insertion
A via can be inserted only when a track is in progress:
- By the Popup menu
- By the hot key (here: 'V').
- By switching to a new copper layer using the suitable hotkey.
### Select the Track width
When the tool is active, the current track width can be changed by the Popup menu (accessible also when creating a track::

Pcbnew retains the last four used sizes.
One can select easily one width or via size, even when a track is in progress.
If the option "Auto Width" is selected, when starting a new track on an existing track, lthe new track will have the same width as the existing track.
## Track edition and correction:
### Change a track:
In many cases redraw a track is enough:
new track (in progress).
When finished:

Pcbnew remove automatically the old track if it is redundant.
### Global Changes:
When right clicking on a track to show the Popup menu, dimensions can be changed for many or all tracks and vias:

New values for track width and via size are the current settings.